## Slide 1: Biomechanics Project A simple algorithm capable of stable gait in a noisy environment?
Joao Fonseca Reis – CMU MRSD
December 2018

## Slide 2
Motivation: A simple algorithm capable of stable gait in a noisy environment?
  High locomotion speed
  Low vertical peak forces
  Low or slowly changing instabilities
  Resilient to “noisy” terrain
  “General” enough (so that you don’t just design your machine for walking)

## Slide 3: Most legged locomotion algorithms focus on each leg independently (not on joint behaviour)
BACKGROUND
Control | Examples of legged locomotion papers | Algorithms using Spring Mass Model
Independent Legs | The spring mass model for running and hoping (R. Blickhan, 1989) | One massless leg + Point mass body Variable Angle of Attack for touchdown
 | Touch-down angle control for spring-mass walking (H Geyer, 2015) | Two massless legs + Point mass body Variable Angle of Attack for touchdown Deadbeat control policy for perturbations
Inter-Dependent Legs | Grounded running in quails: Simulations indicate benefits of observed fixed aperture angle between legs before touch-down (E. Andrada, 2013) | Two massless legs + Point mass body Fixed Angle of Aperture between legs
 | Trunk orientation causes asymmetries in leg function in small bird terrestrial locomotion (E. Andrada, 2017) | Two massless legs + Rigid body trunk Parallel spring and dumper model Fixed Angle of Aperture between legs
Non-exhaustive

## Slide 4: The algorithm used is a fixed aperture angle between the two legs while a leg is in the flight phase
THE MODEL (1/2)
Each leg is a spring of equal stiffness
F
KL
KR
g
The algorithm | 
Both legs flying | Falling body under gravity field (leading leg with 90 angle of attack)
One leg in the air | One foot on the ground with no slippage, not controlled by the algorithm Another foot at angle F measured from the leg in stance
Two legs in stance | Algorithm takes no action whatsoever
m = 80 kg, Kr=Kl=12,000 N/m, g=9.81 m/s^2, l0= 1 m
F = fixed control
m

## Slide 5: The strategy used for looking for stable gaits was plotting Poincare maps
The model (2/2)
Define Success | 
Y(i)=Y(i+1) | Which means it is periodic!
Slope in Poincare map <1 (in module) | Which means it is stable!
Energy elastic = 0 at i+1 | Which means the spring did not “fail to release the ground”
A simple example with one Energy and one F
Used in simulation: E0= 1,665 Joules, F= 20 degrees
The good area…
.. is very close to the bad!
A flying solution!!!
1
3
2

## Slide 6: A “good operating band” delivers a single stable walking gait over several aperture angles but…
RESULTS OBTAINED SO FAR (1/4)
Initial conditions | y0 --> |  |  |  | 
Vx0 | 0.8-0.9 | 0.9-1 | 1-1.1 | 1.1-1.2 | Total Geral
0-1 |  | 0.0% | 21.2% | 0.0% | 7.1%
1-2 | 0.0% | 0.7% | 0.2% | 0.0% | 0.3%
2-3 | 0.0% | 3.4% | 0.0% | 0.0% | 0.7%
3-4 | 0.0% | 12.5% | 0.0% | 0.0% | 3.1%
4-5 | 0.0% | 8.8% | 0.1% | 0.2% | 2.2%
5-6 | 0.0% | 6.8% | 0.1% | 0.3% | 1.7%
6-7 | 0.0% | 8.3% | 0.2% | 0.2% | 2.5%
Total Geral | 0.0% | 7.0% | 0.9% | 0.2% | 2.0%
Success rate across multiple initial conditions
[m/s]
[M]
Successful cases are mostly stationary solutions (Vx0(i)=0)
Note: Scan done for 20 heights (.8 to 1.2 m), 20 energies, 90 different F (in a total of 36,000 runs)
Ex: 1,266 J

## Slide 7: … there this band has no non-grounded running solutions!
RESULTS OBTAINED SO FAR (2/4)
Plotting the success cases
The 1,266 J energy band has no flight solutions!
Each “line” is an energy band
(each point a different F)
The stationary solution (and backwards walking not shown)
Very few “flying solutions”
1
2
3

## Slide 8: Stability may be achieved through irrational periods, which may not be our first choice but deliver long stable walking periods
RESULTS OBTAINED SO FAR (3/4)
Simulation parameters: m = 80 kg; g = 9.81 m/s^2; kR = kL=12,000 N/m; l0 = 1 m; Vx0=3.58 m/s; y0=0.96 m; phi0=28 degrees; x0 = 3 m; Vy0 = 0 m/s; yG=0 m;
[m]
[m]
Leg Forces ratio to robot weight (left leg)
F/(m*g)
s
Example for the 1,226 J band

## Slide 9: When noise is introduced, walking time is more resilient than the final horizontal speed achieved
RESULTS OBTAINED SO FAR (4/4)
Note: By default simulation was always stopped at t=60 s even when the robot had not fallen. 1000 different noise levels were tested.
Noise sampling time: 0.1 s, with noise introduced over the entire simulation
Final horizontal speed for constant noise levels
Horizontal displacement for constant noise levels
Travelled distance falls fast..
1
… and sometimes the robot finishes walking backwards!
2
427 steps
27 steps

## Slide 10
 | Results from literature (highlighted paper) | Results against literature simulations
Forces Symmetry | Symmetric vertical forces1 | In line
Stable solutions | Most of the stable solutions for grounded running | In line (additionally, a stable band may not have any non-grounded stable solution)
Leg Compression | Ratio 1.05 to 1.71 to body weight (BW) | Broadly in line (0.7 to 1.41 BW for different K/m)
Noise resilience (10% leg size) | > 50 steps under single step-up / step down | In line: 27 steps under constant noise equivalent (but possible to have final Vx<0)
Solution Periodicity | Not discussed | Irrational period possible in a stable energy band
RESULTS COMPARISON against literature
1 Nonetheless, experimental data shows positively skewed flattened half-sine pattern) which drives the motivation of the second paper from the same author
Note: While the presented simulations ran for 60 seconds, the literature presentations ran for up to 50 steps

## Slide 11
NEXT STEPS
  Future work may focus on
    Introducing variable stiffness through feed-forward leg placement or muscle pre-activation (as most legged animals do when the adjust their gait)
    Introducing the ability to add/subtract energy from the system through actuation (enabling for example our robot to go up and down a ramp)
    Finding analytically when a gait will be stable/periodic (even if we don’t know where the apex will be located)
    Predicting analytically apex points for any initial condition (e.g. planets XYZ orbits are well defined although until today it is impossible to derive a time dependent equation)

## Slide 12
BACKUP

## Slide 13: First attempt: Brute Force for initial conditions with different height, different speed in x, apex in y
How important is it to have a good predictable model FOR walking dynamics?
Scan the initial conditions where we want to operate in…
m
m/s
… iterate until the next apex is reached (or the ground)
Note: Each color is a different F
Went backwards?
Did “something”?
Straight down!
1
2
3
Note: Scan done for 20 heights (.8 to 1.2 m), 20 energies, 90 different F (in a total of 36,000 runs)

## Slide 14: Contiguous initial conditions can result in massively different outcomes: (deterministic) chaos?
Maybe I am not so confident anymore….
The apple never falls too far from the tree…
… except when it does so… MASSIVELY !!!!